## Slide 1: GPS Navigation
1. Problem Statement and Defining a Path as a Series of Poses

## Slide 2: Problem Statement
given:
  latitude and longitude of four points
  start and end location
perform the following:
  navigate from the start location to within 2m of each of the points and then back to the start location
  points can be visited in any order
  bag data in order to create an xy plot (x is East and y is North) showing the start location, the four points and the motion path of the vehicle (could overlay into Google Earth) ; upload plot to Canvas
  upload your package package to Canvas

## Slide 3
Task 1:
  the start point and the other four points were selected graphically using Google Earth
  how to get the coordinates of these points?
  save and parse .kml file of point locations
point | latitude | longitude
start | 29.64617356 | -82.35372189
1 | 29.64638940 | -82.35384503
2 | 29.64630503 | -82.35405655
3 | 29.64645891 | -82.35412200
4 | 29.64617282 | -82.35411713
Problem Statement

## Slide 4: Coordinate Systems
using the latitude/longitude coordinate data is awkward (for us)
we would like x y in units of meters

## Slide 5: Universal Transverse Mercator (UTM) Coordinates

## Slide 7
UTM coordinate system in Zone 17 R
x axis will be East
y axis will be North
distance units are in meters

## Slide 8: How to convert from lat/long to UTM?
Method 1
  py convert_to_UTM.py input_file.txt output_file.txt
    input file has latitude and longitude separated by a comma on each line
    output file will have Easting, Northing, Zone Number, and Zone letter on each line, separated by a comma
    input file:
      29.6461735604169, -82.3537218948119
      29.6463893972471, -82.3538450308533
      29.6463050340523, -82.3540565509504
      29.6464589142567, -82.3541220000679
      29.6461728159732, -82.3541171317863
    output file: (units of meters ; ‘too many’ significant figures)
      368969.70858622075 , 3280345.325842864 , 17 , R
      368958.06839763390 , 3280369.383803328 , 17 , R
      368937.48358735227 , 3280360.274217328 , 17 , R
      368931.34738749923 , 3280377.4010046674 , 17 , R
      368931.44793484730 , 3280345.6906304797 , 17 , R

## Slide 9: How to convert from lat/long to UTM?
Method 2 http://www.zonums.com/online/coords/cotrans.php?module=13

## Slide 10: Coordinate Systems
UTM in Google Earth
Looks like Google Earth is offering cm level accuracy.

## Slide 11: More about coordinate systems
xveh
yveh
Vehicle Coordinate System
xworld
yworld
World UTM Coordinate System
Pvo

Attach a coordinate system to the vehicle. We chose xveh as ‘forward’ and zveh as ‘up’.
We will keep track of the vehicle pose (position & orientation) in terms of the world system by the coordinates of point Pvo and the angle .
We will use UTM coordinates (units of meters) for the x,y coordinates of worldPvo.
The angle  will be measured from the direction of xworld to xveh in a right-hand sense about zworld.

## Slide 12
Some observations:
direction vectors have no dimensions
xveh
yveh
Vehicle Coordinate System
Pvo

xworld
yworld
World UTM Coordinate System

## Slide 13
xveh
yveh
Vehicle Coordinate System
xworld
yworld
World UTM Coordinate System
Coordinate Transformation Problem
given:
find:
Pvo

P1
2.5 m
1.2 m

## Slide 14
xveh
yveh
Vehicle Coordinate System
xworld
yworld
World Coordinate System
Coordinate Transformation Problem
given:
find:
Pvo

P1
1.2 m
VwoPo
2.5 m

## Slide 15: GPS Nav
How to start the navigation process?
  generate a text file that contains on each line:
    #ptx (m), pty (m), azim_deg (deg), state
  this is a series of desired poses to move through
    a pose is a position and orientation, i.e. (x,y) cords of vehicle origin point and orientation angle θ
  can generate a pose in Google Earth by selecting two points
    first point is the desired position of the vehicle origin point
    the line from the first to the second point will define the desired orientation, i.e. θ
  save the path file as a .kml file
    longitude, latitude, elevation can be obtained from the file
    need to do some Excel ‘magic’ to get a text file that has x, y in UTM on each line
      notepad ++ with find/replace
      web site transform to UTM
    more ‘magic’ to get θ from adjacent pair of points
      excel manipulations
      save a csv file with x, y, θ, state
Start Pose
End Pose
Google Earth path
python3 kml_to_route.py mypath.kml poses.csv
python3 process_pose_list.py poses.csv path_segs.csv

## Slide 16: GPS Nav
  #Easting,Northing,theta (deg),state
  368964.381,3280351.686,126.29,1
  368958.905,3280364.326,116.02,1
  368947.966,3280366.829,-167.45,1
  368941.709,3280360.149,-96.23,1
  368947.337,3280353.54,-24.52,1
  368957.605,3280354.088,8.67,1
  368966.361,3280359.5,41.56,1
  368972.295,3280362.842,-9.84,1
  368978.236,3280358.596,-78.99,1
  368976.551,3280351.907,-136.78,1
  368970.704,3280349.861,172.20,1
  368967.284,3280350.395,155.50,1
Start Pose
End Pose
Google Earth path
This will be our ‘starting’ file.

## Slide 17: Next Up
How do we measure the vehicle pose?
How do I make a ‘smooth continuous’ path through my list of poses?
How do I find the ‘closest pose’ on the path to my current pose?
How do I command the steering (and throttle) to ‘best’ follow the path?