## Slide 1
minimal pub sub
Department of Mechanical and Aerospace Engineering
EML 4930 – ROS2, lecture 2

## Slide 2
https://docs.ros.org/en/foxy/Tutorials.html

## Slide 3: 1. minimal pub / sub
  create 2 nodes in a package named av_min_pub_sub
  node 1:
    minimal publisher from tutorial
  node 2:
    minimal subscriber from tutorial

## Slide 4
Create a workspace
  cd
  mkdir dev_ws_class
  cd dev_ws_class
  mkdir src
  cd src
Create a package
  make sure you are in the src directory
  ros2 pkg create --build-type ament_python av_min_pub_sub
  now have a new directory named av_min_pub_sub in your src directory
  note the files
    package.xml
    setup.py
    setup.cfg
  move into the av_min_pub_sub directory
    there is a file __init__.py that is empty right now
  let’s go ahead and compile our empty package
    go to the dev_ws_class directory
    colcon build if colcon command is not found, install it sudo apt install python3-colcon-common-extensions
  now ‘source’ the package
    go to the dev_ws_class directory and type source install/setup.bash
  now type
    ros2 pkg list and you will see your package av_min_pub_sub in the list

## Slide 5
How do you find out what’s ‘in’ a package?
  ros2 pkg executables turtlesim
  these aren’t the node names, but the commands that will ‘fire up’ the nodes
We’ll now copy the tutorial example and get that running ;
let’s cut and paste the tutorial’s example files
  move into the following directory dev_ws_class/src/av_min_pub_sub/av_min_pub_sub touch my_pub.py touch my_sub.py
  fire up Visual Studio code and open the dev_ws_class folder
  open the my_pub.py and copy/paste into my_pub.py my_sub.py
now setup your package
  package.xml
    fill out the generic stuff
    add the following <exec_depend>rclpy</exec_depend> <exec_depend>std_msgs</exec_depend>
  setup.py
    fill out the generic stuff
    add the following within the console_scripts brackes fo the entry_points field: entry_points={ 'console_scripts': [ 'talker = av_min_pub_sub.my_pub:main’, ‘listener = av_min_pub_sub.my_sub:main’, ], },

## Slide 6
check dependencies
  rosdep install -i --from-path src --rosdistro foxy -y
build it
  make sure you are in your dev_ws directory colcon build
source it
  in your dev_ws, type source install/setup.bash
run the pub node
  ros2 run av_min_pub_sub talker
open a new terminal window, source it, then run it
  ros2 run av_min_pub_sub listener