## Slide 1
custom messages
Department of Mechanical and Aerospace Engineering
EML 4930 – ROS2, lecture 5

## Slide 2
https://docs.ros.org/en/foxy/Tutorials.html

## Slide 3
my_pub
pub_pt.py
‘pub_me’
P
S
geometry_msgs/Vector3
float64 x
float64 y
float64 z
topic name: my_point_topic
P
calc (r, θ) from (x, y)
    x(t) = A1 * cos(0.2*t + π/2) y(t) = A2 * sin(0.6*t) z(t) = 0.0
    t is in sec, t=0 when node starts
    amplitude is in meters
published every 0.5 sec
published whenever a ‘sub’ is received
my_sub_pub
sub_pt_pub_polar.py
‘lets_go’
my_uf_pkg2
av_parameters
node name
python file name
executable name
std_msgs/Float64MultiArray
float64[ ] data
topic name: my_polar_topic

## Slide 4
my_pub
pub_pt.py
‘pub_me’
P
S
geometry_msgs/Vector3
float64 x
float64 y
float64 z
topic name: my_point_topic
P
calc (r, θ) from (x, y)
    x(t) = A1 * cos(0.2*t + π/2) y(t) = A2 * sin(0.6*t) z(t) = 0.0
    t is in sec, t=0 when node starts
    amplitude is in meters
published every 0.5 sec
published whenever a ‘sub’ is received
my_sub_pub
sub_pt_pub_polar.py
‘lets_go’
av_custom_msg
node name
python file name
executable name
av_interfaces/Polar
float64 r_meters
float64 theta_rad
geometry_msgs/Vector3 point
topic name: my_new_polar_topic

## Slide 5: custom message
will put the new message definitions in a new package
  av_interfaces
this will be a C++ package instead of a python package
  don’t worry
go into our workspace/src directory and create a new package
  ros2 pkg create --build-type ament_cmake av_interfaces
move into the my_uf_interfaces directory and create two new directories
  mkdir msg
  mkdir srv
move into the msg directory and create a file Polar.msg ; enter the following in the file
  float64 r_meters
  float64 theta_rad
  geometry_msgs/Vector3 point

## Slide 6: custom message, cont
now we will configure the av_interfaces package
edit the CMakeLists.txt file
  find_package(geometry_msgs REQUIRED)
  find_package(rosidl_default_generators REQUIRED)
  rosidl_generate_interfaces(${PROJECT_NAME}
  "msg/Polar.msg"
  DEPENDENCIES geometry_msgs # Add packages that above messages depend on.
  )

## Slide 7: custom messages, cont
now edit the package.xml file and add
  <depend>geometry_msgs</depend>
  <build_depend>rosidl_default_generators</build_depend>
  <exec_depend>rosidl_default_runtime</exec_depend>
  <member_of_group>rosidl_interface_packages</member_of_group>
go to your workspace directory and colcon build
check that your message exists
  ros2 interface show av_interfaces/msg/Polar
now modify the node my_sub_pub to use this new message
  from av_interfaces.msg import Polar